TEXTURED Floor Care

(For SportRoll, FlashTrack, and Textured ElastiPlus)

Attention Maintenance Personnel and Custodians

Your flooring maintenance schedule has been developed to ensure the superior look of your floor. Sport Court International recommends the following procedures to best maintain your floor. Traffic, usage, and hours of operation will determine the frequency of cleaning and maintenance.

Failure to properly maintain your Connor Sports Flooring® floor may void your warranty.

If you have any questions contact technical services at Connor Sports Flooring® (800)833-7144.

INITIAL CLEANING FOLLOWING INSTALLATION

Equipment and Supplies

1. Walk behind vacuum sweeper

2. Neutral pH cleaner

3. Auto Scrubber (speed must be less then 300 rpm)

4. Light duty nylon bristle pad

5. Electric leaf blower

Procedure for Initial Cleaning

1. Vacuum or blow all dirt and debris from the flooring surface

2. Scrub floor using recommended detergent

• Auto Scrubber application – Dilute detergent according to manufacturer’s recommendation

• Use light duty nylon bristle brush pad

• Apply cleaning solution and scrub in multiple directions without using the vacuum

• Allow cleaning solution to sit for approximately 15 minutes

• Use Auto Scrubber to vacuum up cleaning solution

• Rinse the flooring surface with clean water (repeat until no residue is visible)

ROUTINE CARE – REGULAR TRACK USE

Equipment and Supplies

1. Walk behind vacuum sweeper

2. Neutral pH detergent

3. Auto Scrubber (speed must be less then 300 rpm)

4. Light duty nylon bristle pad

5. Electric Leaf Blower

Procedure for Daily Cleaning

1. Vacuum or blow all dirt and debris from the flooring surface

Procedure for Weekly Cleaning

1. Vacuum or blow all dirt and debris from the flooring surface

2. Scrub floor using recommended detergent

• Auto Scrubber application – Dilute detergent according to manufacturer’s recommendation

• Use light duty nylon bristle brush pad

• Apply cleaning solution and scrub in multiple directions without using the vacuum

• Allow cleaning solution to sit for approximately 10 minutes

• Use Auto Scrubber to vacuum up cleaning solution

• Rinse the flooring surface with clean water (repeat until no residue is visible)